## Slide 1
Semantic Communication for Edge AI
Task-oriented deep joint source–channel coding for image classification
This project compares three ways to transmit an image for remote classification over a bandwidth-constrained noisy channel.
Capstone First Review
Review window: 18–22 August 2026
Presentation slot: 15 minutes
Team / guide details to be added
Rubric: Motivation, Objectives
First Review · 18–22 August 2026
1 / 12

## Slide 2
Project context and basic definition
The application is remote image classification. An edge device observes an image and sends information across a limited, noisy link to a receiver that owns the classifier.
Semantic communication
Semantic communication transmits the information required to preserve meaning or complete a downstream task. It does not require every original source bit to be reconstructed when the task does not need them.
–
Source: an image observed by an edge camera or sensor.
–
Channel constraint: fixed bandwidth and additive wireless noise.
–
Receiver task: predict the correct image class.
Tier 1 is simulation-first. SDR and edge-device deployment are optional later stages.
Rubric: Motivation
Original proposal: Semantic Communication + AI
2 / 12

## Slide 3
Problem statement and research question
Conventional approach
A conventional link compresses an image, protects the bits with a channel code, reconstructs the image at the receiver, and then runs the classifier. Its interfaces optimize image fidelity and bit recovery.
Task-oriented approach
A learned joint system trains the sender and receiver together through a differentiable channel. Its representation can be optimized directly for classification after channel noise.
Research question
At the same bandwidth and channel conditions, can task-aware joint coding preserve classification accuracy better than a properly tuned separated system?
The project reports the measured result even if the learned system does not outperform the baseline.
Rubric: Motivation, Objectives
SPEC §1–2 · completion is independent of outcome
3 / 12

## Slide 4
Related work and the gap addressed
Finite-blocklength communication
Short packets operate below asymptotic capacity and incur non-negligible coding overhead and error probability. [1–4]
Learned image compression
End-to-end transforms improve rate–distortion performance, but reconstruction quality is not the same as task accuracy. [11–17]
Deep joint source–channel coding
DeepJSCC studies continuous learned mappings and graceful degradation over noisy channels. Most image results emphasize reconstruction. [5–10,24]
Task-oriented communication
Learned representations can preserve inference performance, but task awareness and joint coding must be separated experimentally. [18–23]
Gap addressed
A three-way comparison at equal channel uses: adaptive classical image transmission, task-aware digital features, and learned joint coding.
Rubric: Problem Survey, Subject Knowledge
30-source synthesis: docs/literature-review.md
4 / 12

## Slide 5
Project objectives and completion criterion
1.
Implement a normalized simulated AWGN channel and a task-oriented DJSCC system.
2.
Implement a JPEG 2000 + 5G NR LDPC baseline that is tuned on validation data.
3.
Implement a task-aware digital feature system using the same digital physical layer.
4.
Match channel uses, SNR definition, image identity and noise identity across systems.
5.
Freeze all choices before one paired evaluation on the sealed test split.
6.
Report positive, null or negative findings using the preregistered analysis.
Completion criterion
Tier 1 is complete when all three systems are implemented, fairly matched, evaluated once, and reported. Completion does not require a positive result.
Rubric: Objectives, Hypothesis
Formal hypothesis rules are listed in Appendix A
5 / 12

## Slide 6
Systems under comparison
System
Sender and channel path
Receiver output
Classical image link
JPEG 2000 → packet framing → 5G NR LDPC → modulation → AWGN
Reconstructed image → frozen classifier
Digital feature link
Learned features → quantization → same LDPC and modulation → AWGN
Recovered features → task head
Learned joint link
Neural encoder → power normalization → AWGN
Dual-head neural decoder → class
Shared inputs
Same image, dataset split, complex-symbol budget, SNR definition and keyed channel realization.
Data isolation
Validation is used for selection. The test split remains sealed until gate G-12.
Rubric: Subject Knowledge, Objectives
Imagenette-160 headline dataset · normalized AWGN channel
6 / 12

## Slide 7
Experimental controls and fairness rules
Control
Rule
Resource matching
Compare systems at the same complex-symbol budget and SNR definition.
Classical baseline strength
Tune JPEG 2000 quality, LDPC rate and BPSK/QPSK/16-QAM per SNR on validation.
Complete accounting
Count container, CRC, segmentation and filler overhead. Keep decode failures in the denominator.
BLER evidence
Measure every required physical-layer identity. Missing evidence is not interpreted as zero error.
Attribution
Use the digital feature system to separate task-aware representation from joint coding.
Evaluation
Use paired per-image outcomes and one sealed test campaign after all choices are frozen.
Rubric: Subject Knowledge, Objectives
SPEC BR-4, BR-10/11, ER-3/9/10
7 / 12

## Slide 8
Engineering and gate evidence—not learned-vs-classical results
Gate
Status
Recorded evidence
Meaning
G-1
PASS
898/1,000 = 89.8% validation accuracy
The reference classification task is viable.
G-7
PASS
1.64 M parameters; 48.68 s per epoch; 1.004 GiB VRAM
The planned DJSCC model fits the available GPU.
G-2
PASS
Golden vectors and BLER waterfall checks within 0.5 dB
The digital physical layer passes conformance checks.
W4
PASS
Bounded JPEG 2000 → LDPC → AWGN → decode run
The classical pipeline and evidence path work end to end.
G8_C
ACTIVE
748 / 3,213 authenticated BLER units
The full BLER table and operating-point selection are not complete.
No learned-versus-classical headline result exists yet. Bounded integration evidence is not presented as a scientific comparison.
Rubric: Subject Knowledge
Authenticated G-1, G-2, G-7, W4 and G8_C records · test access = 0
8 / 12

## Slide 9
Remaining work and review dates
Period / gate
State
Work
Output
Now · G8_C
Active
Complete BLER characterization and freeze the table
Inputs for G-8
G-8
Planned
Select operating ratios and classical configurations
Frozen baseline choices
W5–W8
Planned
Train DJSCC; calibrate λ; implement digital feature control
Frozen learned systems
W9–W11
Planned
Validation rehearsal; freeze; one test campaign
Hypothesis decisions
W13–W17
Planned
Demo, report, poster and final review preparation
Final package
First Review: 18–22 Aug · Second Review: 29 Sep–3 Oct · Final Review: 17–21 Nov · Report due: 20 Nov
W16 is reserved for report contingency. It is not available for new experiment scope.
Rubric: Time Plan
docs/gantt-plan.md · unfinished stages are shown as unfinished
9 / 12

## Slide 10
Scope, deliverables, and decisions requested
Required Tier 1 scope
Simulation-based comparison of the three systems on image classification over normalized AWGN, with one sealed test campaign and paired analysis.
Optional later scope
Conducted SDR replay and Raspberry Pi deployment are stretch goals after gate G-5. No hardware has been purchased.
Technical claim boundary
OpenJPEG 2.5.4 and a TS 38.212-derived LDPC/rate-matching chain over abstract AWGN. This is not a full 5G NR link claim.
Decision requested
Confirm the task boundary, the three-system comparison, the fairness controls, and simulation-first Tier 1 as a sufficient completion path.
Outstanding human item
The guide's dated acknowledgement of the simulation-first, no-required-hardware path is still pending.
Rubric: Objectives, Subject Knowledge
PR-3 standards register · PR-9 deployment dossier · guide acknowledgement PENDING
10 / 12

## Slide 11
Hypotheses and analysis plan
H1 — Low-SNR separation (confirmatory primary)
Comparator: learned versus classical_adaptive at the headline ratio. A grid point qualifies when the studentized paired mean √N·Δ̂(s)/σ̂(s) exceeds 1.96. Let R_obs be the longest run of consecutive qualifying points at or below the training SNR. H1 is supported only if R_obs ≥ 3 and the calibrated run p-value ≤ 0.05.
H2 — Graceful versus cliff
The fixed classical curve must show the preregistered large drop while the learned curve remains within its smaller-drop bound.
H3 — Convergence
The paired learned-minus-classical gap must contract across SNR. A crossover is reported if observed but is not required.
H4 — Attribution
Joint coding is credited only if the learned joint system also exceeds the task-aware digital feature control under the H1 procedure.
All hypotheses use paired per-image outcomes. The test split is opened once after gate G-12.
Rubric: Hypothesis, Subject Knowledge
Exact formal protocol: SPEC §2 and ER-10
11 / 12

## Slide 12
First Review rubric map and sources
Criterion
Slides
Evidence
Motivation
2–3
Application context and problem statement
Objectives
3, 5–7, 10
Systems, completion criterion and review ask
Hypothesis
5, 11
Outcome-independent completion and formal rules
Problem Survey
4, 12
30-source literature synthesis
Subject Knowledge
6–8, 10–11
System design, controls, evidence and scope
Time Plan
9
Gate-ordered schedule and fixed review dates
Selected references
[1] Shannon, 1948.
[3] Polyanskiy, Poor & Verdú, 2010.
[4] Kostina & Verdú, 2013.
[5] Bourtsoulatze, Kurka & Gündüz, 2019.
[11] Ballé, Laparra & Simoncelli, 2017.
[17] Blau & Michaeli, 2018.
[18] Jankowski, Gündüz & Mikolajczyk, 2021.
[20] Xie et al., 2021.
Evidence records
G-1: results/reference_classifier/g1_adjudication.json G-7: results/profiling/g7_djscc_profile.json G-2 / W4 / G8_C: results/baseline/
Refresh G8_C status from instructions/RESUME.md on submission day.
Rubric: Problem Survey, Time Plan, Subject Knowledge
Full literature review contains 30 synthesized references
12 / 12