## Slide 1
CAPSTONE · FIRST REVIEW · 18–22 AUG 2026
§ 01
Semantic Communication for Edge AI
Can a machine communicate what matters for a task—without sending every pixel perfectly?
EDGE CAMERA
observes an image
LIMITED + NOISY LINK
cannot carry everything reliably
RECEIVER AI
only needs the correct class
THESIS
Train the sender and receiver together so the information needed for classification survives the link—then compare it fairly with a strong conventional system.
A simulation-first capstone with an optional real-radio demonstration later.
MOTIVATION
OBJECTIVES
Official scope: task-oriented DJSCC for image classification · First Review baseline 12 Aug 2026
01/12

## Slide 2
CAPSTONE · FIRST REVIEW · 18–22 AUG 2026
§ 02
The AI is only as useful as the link feeding it
Imagine a remote camera sending images to a server that decides what it sees.
REAL-WORLD TENSION
1
The sensor is constrained
Bandwidth, latency and energy are limited at the edge.
2
The wireless link is imperfect
Noise can corrupt a short message or make decoding fail.
3
The receiver has a narrow goal
For classification, the final question is often simply: what is in the image?
DESIGN QUESTION
Why spend the entire link budget reconstructing every pixel if the receiver ultimately needs a task decision?
The project tests this question; it does not assume the learned method must win.
Goal: preserve classification performance when communication resources are scarce and the link becomes noisy.
MOTIVATION
Original proposal: Semantic Communication + AI · edge/IoT application framing
02/12

## Slide 3
CAPSTONE · FIRST REVIEW · 18–22 AUG 2026
§ 03
From bit-perfect delivery to task success
CONVENTIONAL COMMUNICATION
Compress the image → protect the bits → reconstruct the file → classify it
Primary objective: recover source bits and pixels
TASK-ORIENTED COMMUNICATION
Learn a representation → send it through noise → recover what the task needs
Primary objective: retain information useful for classification
EXPECTED SIGNATURE
As the link worsens, a separated chain may hit a decoding cliff; a learned joint system may degrade more gradually.
IMPORTANT CONTROL
A digital system can also send learned features—so the experiment includes that third arm.
Research question: does the task-oriented joint design help after bandwidth, noise and comparison strength are matched fairly?
MOTIVATION
OBJECTIVES
Conceptual behavior only—not measured project results · formal three-arm experiment begins on slide 6
03/12

## Slide 4
CAPSTONE · FIRST REVIEW · 18–22 AUG 2026
§ 04
How prior research leads to this project
Finite blocklength
[1–4]
Rate backs off from capacity; source and channel dispersions interact.
OPEN ISSUE
Need measured practical short-packet loss.
Learned compression
[11–17]
End-to-end transforms and entropy priors improve rate–distortion.
OPEN ISSUE
Reconstruction optimization is not task optimization.
DeepJSCC
[5–10,24]
Continuous learned mappings exhibit graceful degradation under mismatch.
OPEN ISSUE
Most image studies foreground reconstruction quality.
Task-oriented communication
[18–23]
Learned representations can preserve remote inference under link constraints.
OPEN ISSUE
Task awareness must be separated from joint coding.
Gap carried forward: three-way attribution at equal channel uses, with a strong adaptive classical comparator and paired failures retained.
PROBLEM SURVEY
SUBJECT KNOWLEDGE
30-source synthesis in docs/literature-review.md · references [1]–[23]
04/12

## Slide 5
CAPSTONE · FIRST REVIEW · 18–22 AUG 2026
§ 05
What we will build—and what counts as success
OBJECTIVES
1.
Build a reproducible normalized-AWGN DJSCC pipeline.
2.
Implement a standards-derived, non-strawman JPEG 2000 + NR LDPC baseline.
3.
Tune classical quality, code rate and modulation on validation only.
4.
Add the task-aware digital feature control for attribution.
5.
Evaluate paired image outcomes once on the sealed test split.
6.
Report positive, null or negative outcomes under one frozen protocol.
H1 · PRIMARY
Low-SNR separation: learned − classical_adaptive
A point qualifies when √N·Δ̂(s)/σ̂(s) > 1.96. H1 is supported only if the longest run R_obs contains at least three consecutive qualifying points at or below the training SNR and the calibrated run p-value ≤ 0.05.
Effect size of record: mean paired accuracy difference over the full low-SNR region.
H2
Graceful vs cliff
Fixed classical curve drops ≥30 pp while learned drops ≤15 pp over the frozen window.
H3
Convergence
Paired gap trends toward zero across SNR; crossover is reported, not required.
H4
Attribution
Credit joint coding only if DJSCC also exceeds the task-aware digital control under the H1 rule.
OBJECTIVES
HYPOTHESIS
Exact decision protocol: SPEC §2 and ER-10 · H1 is the sole confirmatory primary
05/12

## Slide 6
CAPSTONE · FIRST REVIEW · 18–22 AUG 2026
§ 06
The experiment in one picture
IMAGENETTE-160
canonical 160 × 160 RGB preprocessing
stable sample ID + split manifest
CLASSICAL IMAGE LINK
JPEG 2000 packetise + CRC NR LDPC + modulation
AWGN keyed noise
decode reconstruct frozen classifier
DIGITAL TASK-FEATURE LINK
learned features quantize same LDPC + modulation
AWGN keyed noise
decode feature task head
LEARNED JOINT LINK
neural encoder power normalize
AWGN keyed noise
dual-head decoder reconstruction + class
Per-image paired row: verdict + exact k + measured Eₛ + noise identity + task outcome
TEST SEALED → G-12
SUBJECT KNOWLEDGE
OBJECTIVES
SPEC SR-4, SR-17, BR-4, ER-9 · src/data/test_access.py is the sole release boundary
06/12

## Slide 7
CAPSTONE · FIRST REVIEW · 18–22 AUG 2026
§ 07
How we keep the comparison fair
Equal resource
Same complex-symbol budget k and Eₛ/N₀ definition; realized symbol energy is logged.
Strong comparator
JPEG 2000 quality, LDPC rate and BPSK/QPSK/16-QAM tune per SNR on validation.
Exact accounting
Container, CRC, code-block and filler bytes count; decode failures remain in the denominator.
Measured BLER
Every required physical identity is characterized; missing evidence is never treated as zero BLER.
Outage policy
Constant-class fallback is measured from validation counts—100/1,000—not assumed as 1/10.
Classifier control
Clean and artifact-finetuned classifier passes separate codec shift from link failure.
Attribution arm
Quantized learned features traverse the same digital chain, isolating task awareness from joint coding.
One test campaign
All choices freeze before G-12; paired inference retains complete image × system trajectories.
Fail-closed rule: uncharacterized, infeasible and failed cases are explicit outcomes—not silently dropped rows.
SUBJECT KNOWLEDGE
OBJECTIVES
BR-4, BR-10/11, ER-3/4/9/10 · W4 integration adjudication
07/12

## Slide 8
CAPSTONE · FIRST REVIEW · 18–22 AUG 2026
§ 08
Engineering and gate evidence—not learned-vs-classical results
NO HEADLINE COMPARISON EXISTS YET · bounded smoke is integration evidence, not scientific outcome evidence
G-1 · classifier
89.8%
898/1,000 validation top-1 88% preregistered floor · PASS
G-7 · feasibility
1.64 M
DJSCC parameters · batch 32 48.68 s/epoch · 1.004 GiB VRAM
G-2 · digital PHY
≤ 0.0037 dB
observed waterfall displacement all three modulations within 0.5 dB · PASS
W4 · integration
end-to-end
JPEG 2000 → LDPC → AWGN → decode records + verifier · bounded PASS
G8_C · CURRENT
748 / 3,213
authenticated full-strength BLER units source epoch 2 registered · resumable campaign paused
BLER table: not frozen selection / inference / training / test: 0
Interpretation: the reference task, computational budget and digital chain are verified; the comparison itself remains ahead.
SUBJECT KNOWLEDGE
Authenticated records: G-1, G-2, G-7, W4 and G8_C · test split access = 0
08/12

## Slide 9
CAPSTONE · FIRST REVIEW · 18–22 AUG 2026
§ 09
Project Gantt chart
WORKSTREAM
AUGUST
SEPTEMBER
OCTOBER
NOVEMBER
BLER characterization + G-8
PAUSED → PLANNED
First Review package
DJSCC training + calibration
PLANNED
Digital control + validation
PLANNED
Freeze + single test campaign
PLANNED
Demo + optional replay
PLANNED
Report, audit + final review
PLANNED
W16 contingency
Review dates: 18–22 Aug · 29 Sep–3 Oct · 17–21 Nov · report due 20 Nov
W16 is report contingency—not room for new experiment scope.
TIME PLAN
Detailed dependencies and acceptance evidence: docs/gantt-plan.md
09/12

## Slide 10
CAPSTONE · FIRST REVIEW · 18–22 AUG 2026
§ 10
What this First Review should confirm
RESEARCH SCOPE
Project boundary
One narrow task: classify an image after communication over a bandwidth-limited noisy link. The sender runs an encoder; the receiver owns the task head. That deployment split is fixed. Tier 1 uses a normalized simulated AWGN channel so the scientific comparison is controlled and reproducible. The result may be positive, null or negative.
IMPLEMENTATION
Deployment ladder
TIER 1 · required Simulation-first, offline and reproducible. TIER 2 · stretch after G-5 Conducted SDR I/Q replay; prerecorded outcome expected. TIER 3 · stretch Edge placement only if latency and procurement gates pass. Candidate: HackRF One + attenuation chain + RTL-SDR; no purchase yet.
PANEL ASK
Decision requested
Confirm that the project asks the right question and compares the systems fairly: • image-classification is the task • communication resources are matched • the classical baseline is strong • the digital feature arm supports attribution • simulation-first Tier 1 is sufficient Guide acknowledgement: PENDING
TECHNICAL BOUNDARY
OpenJPEG 2.5.4 + TS 38.212-derived LDPC/rate matching over abstract AWGN—not a full 5G NR link claim
No guaranteed win, measured energy saving or real-radio generalization; completion means executing the preregistered protocol.
SUBJECT KNOWLEDGE
OBJECTIVES
PR-3 standards register · PR-9 deployment dossier · guide acknowledgement remains PENDING
10/12

## Slide 11
CAPSTONE · FIRST REVIEW · 18–22 AUG 2026
§ 11
Explicit First Review rubric-to-slide map
CRITERION
SLIDES
EVIDENCE EXPOSED IN THE DECK
Motivation
2–3
Short packets, fixed k, task accuracy, finite-blocklength costs
Objectives
3, 5–7, 10
Three-arm build, fair protocol, attribution control, decision ask
Hypothesis
5
Exact H1 run rule; H2–H4 preregistered; crossing not required
Problem Survey
2, 4, 12
30-source synthesis across four literature families
Subject Knowledge
3–8, 10
AWGN, LDPC, JPEG 2000, fairness, evidence and scope boundary
Time Plan
9
Gate-ordered critical path and fixed review/report dates
Final PASS still requires the real PPT review, four-member rehearsal, guide acknowledgement and annotated review-1-basis tag.
RUBRIC MAP
Six criteria × five sub-marks · 30 scaled to 10 · final human readiness remains evidence-based
11/12

## Slide 12
CAPSTONE · FIRST REVIEW · 18–22 AUG 2026
§ 12
Selected references and evidence provenance
SELECTED LITERATURE
[1] Shannon, A Mathematical Theory of Communication, 1948.
[2] Gastpar, Rimoldi & Vetterli, To Code, or Not to Code, 2003.
[3] Polyanskiy, Poor & Verdú, Finite Blocklength, 2010.
[4] Kostina & Verdú, Lossy JSCC at Finite Blocklength, 2013.
[5] Bourtsoulatze, Kurka & Gündüz, DeepJSCC, 2019.
[6] Kurka & Gündüz, DeepJSCC-f, 2020.
[7] Kurka & Gündüz, Bandwidth-Agile DeepJSCC, 2021.
[11] Ballé, Laparra & Simoncelli, Learned Compression, 2017.
[12] Ballé et al., Scale Hyperprior, 2018.
[17] Blau & Michaeli, Perception–Distortion, 2018.
[18] Jankowski, Gündüz & Mikolajczyk, Wireless Retrieval, 2021.
[19] Shao, Mao & Zhang, Task-Oriented Edge Inference, 2021.
[20] Xie et al., Deep Learning Enabled Semantic Communication, 2021.
REPOSITORY EVIDENCE
G-1
results/reference_classifier/g1_adjudication.json
89.8% validation; test sealed
G-7
results/profiling/g7_djscc_profile.json
1.64M params; measured epoch/VRAM
G-2
results/baseline/g2/g2_adjudication.json
golden vectors + BLER conformance
W4
results/baseline/w4/integration_adjudication.json
bounded end-to-end integration
G8_C
results/baseline/g8/campaign_state.json
authenticated characterization cursor
Spec
spec/SPEC.md
normative hypotheses and requirements
Plan
docs/gantt-plan.md
dates, gates and current status
Deploy
docs/deployment-dossier.md
simulation-first + SDR stretch
Refresh G8_C status from instructions/RESUME.md on submission day.
PROBLEM SURVEY
SUBJECT KNOWLEDGE
Full 30-reference synthesis: docs/literature-review.md · all evidence verified from repository records
12/12