## Slide 1
Semantic Communication + AI
Learning what to send for a remote image-classification task
An edge camera sees an image. A server across a limited, noisy link must recognize it. We compare a normal communication system with systems that learn what information to send.
Capstone First Review
Review window: 18–22 August 2026
Presentation slot: 15 minutes
Team and guide details to be added
Rubric: Motivation, Objectives
First Review · 18–22 August 2026
1 / 12

## Slide 2
What problem are we solving?
1
Observe
An edge camera sees an image.
2
Communicate
The link has limited bandwidth and added noise.
3
Classify
A server decides what the image contains.
4
Question
Must the camera send every image detail?
Why this matters
Sending a complete high-quality image can be expensive when the receiver only needs a correct task decision.
The project asks whether a learned system can preserve that decision using the same channel budget.
Rubric: Motivation, Objectives
The task is remote image classification over a limited noisy link
2 / 12

## Slide 3
How is this normally done?
Image
camera input
Compress
JPEG 2000
Protect bits
LDPC + modulation
Add noise
simulated channel
AI classifier
recovered image → ResNet-18
Compression
reduces the number of source bits.
Error correction
adds controlled redundancy so damaged bits can be recovered.
Modulation
maps protected bits to symbols sent through the channel.
AI classifier
a frozen ResNet-18 maps the recovered image to class logits.
Limitation: the communication stack is designed separately from the AI objective, even though task accuracy is the final metric.
Rubric: Motivation, Subject Knowledge
Headline baseline: JPEG 2000 + TS 38.212-derived LDPC over AWGN
3 / 12

## Slide 4
What are we proposing?
Image
sender input
Learned sender
decides what to send
Noisy link
limited bandwidth
Learned receiver
recovers task information
Class
final decision
The basic idea
Train the sender and receiver together using labeled images and simulated noise. The system can then learn which image information helps the receiver make the correct decision.
Why not send the label?
The project fixes the deployment split: the sender has an encoder, while the receiver owns the decoder and classifier. Sending a label would move the full task model to the sender and test a different system.
Technical name: deep joint source–channel coding (DJSCC)
AIML method: supervised end-to-end training · model and loss details follow in the methodology
Rubric: Motivation, Objectives, Subject Knowledge
DJSCC = deep joint source–channel coding
4 / 12

## Slide 5
Literature survey and research gap
Short-packet communication
Finite packets pay coding overhead and can fail abruptly.
Measure the practical baseline instead of assuming ideal capacity. [1–4]
Learned image compression
Neural transforms learn compact image representations.
Good reconstruction quality is not the same as good AI task accuracy. [11–17]
DeepJSCC
Neural encoders and decoders can learn continuous channel mappings.
Most image studies emphasize reconstruction rather than classification. [5–10,24]
Task-oriented edge AI
Learned features can preserve inference under link limits.
Representation learning and joint coding are often not isolated. [18–23]
Gap addressed
A controlled three-way experiment that separates neural representation learning from joint channel coding at equal channel use.
Rubric: Problem Survey, Subject Knowledge
30-source synthesis: docs/literature-review.md
5 / 12

## Slide 6
Problem statement, research question and objectives
Problem statement
An edge camera has a limited noisy link, while the server only needs a correct class decision. A conventional system tries to rebuild the image first. The project tests whether a learned system can protect the decision more directly.
Research question
At the same bandwidth and channel conditions, can the learned joint system preserve classification accuracy better than a tuned conventional system, and does joint training explain any remaining gain?
Objectives
1.
Build and train the learned sender and receiver models.
2.
Build a digital feature system that separates task awareness from joint training.
3.
Match channel use, SNR, image identity and noise across all systems.
4.
Freeze all learned models and choices, then run one paired test campaign.
Completion depends on executing the fixed protocol correctly, not on obtaining a favorable result.
Rubric: Motivation, Objectives
Objectives are stated as completion work, not promised outcomes
6 / 12

## Slide 7
Proposed methodology
Imagenette-160 · same image and split · same complex-symbol budget · same SNR · same keyed noise
System
Transmission path
Scientific role
Classical + AI
JPEG 2000 → LDPC → AWGN → recovered image → frozen ResNet-18
Conventional reference
AI feature control
Shared neural encoder → quantization → same digital PHY → shared task head
Isolates representation learning
Neural DJSCC
Residual encoder → normalization → AWGN → dual-head neural decoder
Tests end-to-end neural coding
Evaluation controls
Train with supervised CE + λMSE; tune on validation only; freeze before test access; retain failed transmissions; compare paired per-image AI outcomes.
The test split remains sealed until gate G-12. No test result exists at First Review.
Rubric: Objectives, Subject Knowledge
Three systems · one shared task, resource budget and channel definition
7 / 12

## Slide 8
Research hypotheses
Primary hypothesis (H1)
At difficult low-SNR conditions, the learned joint system will preserve classification accuracy better than the tuned conventional system across a consecutive region—not at only one isolated point.
Formal decision rule
Comparator: learned versus classical_adaptive at the headline ratio. A point qualifies when √N·Δ̂(s)/σ̂(s) > 1.96. R_obs is the longest consecutive qualifying run at or below the training SNR. H1 is supported only if R_obs ≥ 3 and the calibrated run p-value ≤ 0.05.
Effect size: the mean paired accuracy difference over the full low-SNR region. A curve crossing is reported if observed, but is not required.
H2
Does a fixed conventional configuration show a cliff while the learned system degrades more gradually?
H3
Does the learned–classical accuracy gap contract as SNR improves?
H4
Does the learned joint system also exceed the task-aware digital feature control?
Outcome rule: support, no support or an adverse result are all valid findings. The protocol does not change after test access.
Rubric: Hypothesis, Subject Knowledge
Primary metric: paired top-1 AI inference accuracy · exact protocol: SPEC §2
8 / 12

## Slide 9
Preliminary work and feasibility
Item
Observed evidence
What it tells us
What it does not tell us
AI task
ResNet-18 from scratch: 89.8% validation
The classification task and clean reference model are viable.
Validation only; test is sealed. (G-1)
Learned model
DJSCC: 1.64 M parameters
The planned model fits the available RTX 4060.
A feasibility profile, not training. (G-7)
Digital link
Golden vectors and BLER conformance pass
The channel-coding implementation behaves as expected.
Conformance evidence, not the full table. (G-2)
Full pipeline
Bounded conventional run completes
Compression, coding, channel and records work together.
Integration evidence, not a comparison. (W4)
G8_C
BLER characterization complete
Pascal successor table is frozen from measured points.
No learned-system result. (G8_C)
G8_D
Validation tooling complete
D0–D7 GREEN; codec/cache/record/resume tooling is ready.
Bounded smoke is not the full campaign. (G8_D)
G8_E/E0 is released but full validation/pass one has not started. Training/fine-tuning, learned-vs-classical results and test evaluation are not available.
Rubric: Subject Knowledge
Engineering and gate evidence only · no learned-versus-classical result
9 / 12

## Slide 10
Project Gantt chart
Workstream
AUG
SEP
OCT
NOV
G8_C BLER characterization
G8_D validation-measurement tooling
G8_E validation + pass one / G-8
Learned model training + tuning
PLANNED
Digital feature system + validation
PLANNED
Freeze + single test campaign
PLANNED
Demo + optional replay
PLANNED
Report, audit + final review
PLANNED
W16 contingency
Review dates: 18–22 Aug · 29 Sep–3 Oct · 17–21 Nov · report due 20 Nov
G8_C and G8_D are complete. G8_E/E0 is next but not started; all later bars remain planned. W16 is report contingency.
Rubric: Time Plan
Detailed dependencies and acceptance evidence: docs/gantt-plan.md
10 / 12

## Slide 11
Applications, project scope and risks
Edge AI application
Remote cameras and edge sensors send task-relevant information to a receiver-side AI model when bandwidth, latency or link reliability is limited. This represents split edge/cloud inference.
AI/ML contribution
Channel-robust neural representation learning; a residual encoder and dual-head decoder; CE + λMSE multi-task training; and a digital feature control that isolates the value of joint coding.
Main risks and controls
BLER work is incomplete: resume from the authenticated checkpoint. A hypothesis may not be supported: report the result without retuning. Hardware adds confounders: keep it as gated stretch work.
Technical claim boundary
Tier 1 is a simulation-based AI experiment over normalized AWGN. OpenJPEG 2.5.4 and TS 38.212-derived LDPC are controls; no complete 5G NR radio or required hardware is claimed.
Outstanding human item: the guide's dated acknowledgement of the no-required-hardware path remains pending.
Rubric: Motivation, Subject Knowledge, Objectives
Circular clause 5 · PR-3 standards register · PR-9 deployment dossier
11 / 12

## Slide 12
Summary and next steps
Project summary
Problem
Edge AI inference must operate over a limited noisy link.
AI/ML method
Train a residual neural encoder and dual-head decoder through a differentiable channel.
Evaluation
Measure Imagenette-160 classification at matched channel use against two controlled baselines.
Next work
Finish characterization, train and freeze the models, then run the paired test campaign once.
Six-criterion rubric map
Motivation
2–4, 6, 11
Objectives
6–7, 11–12
Hypothesis
8
Problem Survey
5
Subject Knowledge
3–5, 7–9, 11
Time Plan
10
First Review position
The AI/ML method, controlled evaluation protocol, feasibility evidence and completion plan are defined. Final neural training and learned-versus-classical results remain future work.
Rubric: Motivation, Objectives, Hypothesis, Problem Survey, Subject Knowledge, Time Plan
Full package: deliverables/review-1/first-review-package.md
12 / 12